## Slide 1
BUILDING AND SECURING A SMALL NETWORK
01
Supervisor: Eng. Khaled Abd Rabo

## Slide 2
02
MISSION CONTENT
Network Design
01
Devices Configuration
02
Security Implementation and Testing
03

## Slide 3
03
NETWORK DESIGN
Design the Physical Layout
01
  Router: Connect different network segments/VLANs.
  Switches: Connected with multiple devices within different segments/VLANs.
  A web server: a sever that hosts and delivers web traffic to users over the internet handling requests via protocols like HTTP/HTTPS.
  A database server: a server that provides database services to other computers or applications, enabling the storage, retrieval, and management of data.

## Slide 4
04
The main network consists of one router and 2 switches, Switch 1 contains 2 end devices in VLAN 10, 2 end devices in VLAN 20, and connects the administrator’s device in vlan 99, As for switch 2, it contains 2 end devices in VLAN 10, 4 end devices and a database server in VLAN 20, and web server in VLAN 50.

## Slide 5
05
Network Segments
We have four main VLANs which are:
  VLAN 10 (HR): For HR department devices.
  VLAN 20 (IT): For IT department devices.
  VLAN 50 (DMZ): Contains the web server and is accessible by every on the internet.
  VLAN 99 (Management): For managing the network device via SSH remote connection protocol.
  VLAN 100 (Native): Changed the native VLAN to be VLAN 100 instead of the default VLAN 1.

## Slide 6
06
  Configuring Basic Devices Settings
  Naming devices
  Securing privileged access
  Securing console line
  Securing VTY lines
  Encrypting passwords
  Setting a banner
  Setting the time and date
Phase - 1 (Initial Configuration)

## Slide 7
07
Configuring SSH For Remote Management
1.Configuring a domain name for the device
2.Generating RSA keys and choosing the modulo
bit size to be 2048
3.Creating an SSH user with username and
password

## Slide 8
08
Configuring SSH For Remote Management
4.Allowing VTY logins for two minutes if three failed login attempts occur within 60 seconds.
5.Using SSH version 2

## Slide 9
09
  Creating VLAN on the switches
  Configuring access ports on the switches
  Configuring SVIs
  Configuring trunk ports on the switches
  Configuring router-on-a-stick inter-VLAN routing on the router
  Enabling the Physical Interface
Phase - 2 (Implementing VLANs)

## Slide 10
10
  Implementing Port Security
1. Shutting Down Unused Ports.
2. Mitigating MAC Address Table Overflow Attacks
  Enabling Port Security
Phase - 3 (Security Measures)

## Slide 11
11
2. Mitigating MAC Address Table Overflow Attacks (continue)
  Setting the max. number of secure MAC address to 1
  Configuring the learning process for the MAC address to sticky
  Setting the Port Security Violation Mode to restrict

## Slide 12
12
SECURITY MEASURES
1.Access control:
  Inbound and Outbound Rules: Define rules to control traffic based on IP addresses, ports, and protocols.
  Access Control Lists (ACLs): Restrict access to sensitive segments.
2.Network Segmentation:
  VLANs: Use VLANs to separate different network segments.
  Inter-VLAN Routing: Control traffic between VLANs using router-on-a-stick method.

## Slide 13
3.Implemented features that considers security
  Using enable secret instead of enable password for more secure password by using md5 hashing algorithm.
  Changing the default native & management VLANs from VLAN 1 to be VLAN 99 (Management) and VLAN 100 (Native).
  Using SSH version 2 instead of the legacy version 1.
13

## Slide 14
3.Implemented features that considers security
  Using a large modulus space with a 2048 bits when generating the RSA keys for SSH communication encryption.
  Setting a password policy that restricts using a password length of min. size of 12 characters when configuring the network devices.
  Allowing VTY logins for two minutes if three failed login attempts occur within 60 seconds.
14

## Slide 15
15
SECURITY MEASURES
4.Mitigating VLAN Hopping Attacks
  Disable DTP (auto trunking) negotiations on non-trunking ports by using the switchport mode access interface configuration command.
  Disable unused ports and put them in an unused VLAN.
  Manually enable the trunk link on a trunking port by using the switchport mode trunk command.
  Disable DTP (auto trunking) negotiations on trunking ports by using the switchport nonegotiate command.
  Set the native VLAN to a VLAN other than VLAN 1 by using the switchport trunk native vlan vlan_number command.
03

## Slide 16
  Strong Password Policies: Encourage the use of complex, unique passwords.
  Regular Software Updates: Ensure that all software, firmware, and devices are up-to-date.
  Network Monitoring: Continuous monitoring of traffic to detect unusual activities.
  Backup and Recovery Plan: Regularly backup critical data and have a disaster recovery strategy.
Best Practices for Network Security
16

## Slide 17
THANK
YOU
17