## Slide 1
Studio Shodwe
01
BUILDING AND SECURING A SMALL NETWORK

## Slide 2
Studio Shodwe
02
MISSION CONTENT
Network Design.
01
Configuration and Implementation
02
Security Implementation and Testing
03

## Slide 3
Studio Shodwe
03
NETWORK DESIGN.
Design the Physical Layout
01
  Routers: Connect different network segments.
  Switches: Connect multiple devices within the same segment.
  A web server: a system that hosts and delivers web pages to users over the internet handling requests via protocols like HTTP/HTTPS.
  A backup server: stores copies of data from other systems, providing a safeguard to restore information in case of data loss, corruption, or failure.

## Slide 4
Studio Shodwe
04
Segment the Network
  IT Department: Connect via switches to a dedicated segment.
  Server Segment: Isolate servers in a separate segment for security and performance.

## Slide 5
Studio Shodwe
05
02
Configuration Security Implementation and Testing
  Implementing Port Security
1. Shutting Down Unused Ports.
Switch(config)# interface range <interface-id>
Switch(config-if)# shutdown
2. Mitigating MAC Address Table Overflow Attacks
  Enabling Port Security
Switch(config)# interface <interface-id>
Switch(config-if)# switchport mode access
Switch(config-if)# switchport port-security

## Slide 6
Studio Shodwe
06
2. Mitigating MAC Address Table Overflow Attacks (continue)
  Setting the max. number of secure MAC address to 1
Switch(config-if)# switchport port-security maximum 1
  Configuring the learning process for the MAC address to sticky
Switch(config-if)# switchport port-security mac-address sticky
  Setting the Port Security Violation Mode to restrict
Switch(config-if)# switchport port-security violation restrict

## Slide 7
Studio Shodwe
07
SECURITY MEASURES
  Access control:
  Inbound and Outbound Rules: Define rules to control traffic based on IP addresses, ports, and protocols.
  Access Control Lists (ACLs): Restrict access to sensitive segments.
2.Network Segmentation:
  VLANs: Use VLANs to separate different network segments.
  Inter-VLAN Routing: Control traffic between VLANs using a Layer 3 switch or router.
3.Implemented features that considers security
  Using enable secret instead of enable password for more secure password by using md5 hashing algorithm.
  Changing the default native & management VLANs from VLAN 1 to be VLAN 99 (Management) and VLAN 100 (Native).
  Using SSH version 2 instead of the legacy version 1.
  Using a large modulus space with a 2048 bits when generating the RSA keys for SSH communication encryption.
  Setting a password policy that restricts using a password length of min. size of 12 characters when configuring the network devices.
  Allowing VTY logins for two minutes if three failed login attempts occur within 60 seconds.
03

## Slide 8
Studio Shodwe
08
SECURITY MEASURES
4.Mitigating VLAN Hopping Attacks
  Disable DTP (auto trunking) negotiations on non-trunking ports by using the switchport mode access interface configuration command.
  Disable unused ports and put them in an unused VLAN.
  Manually enable the trunk link on a trunking port by using the switchport mode trunk command.
  Disable DTP (auto trunking) negotiations on trunking ports by using the switchport nonegotiate command.
  Set the native VLAN to a VLAN other than VLAN 1 by using the switchport trunk native vlan vlan_number command.
03

## Slide 9
  Strong Password Policies: Encourage the use of complex, unique passwords.
  Regular Software Updates: Ensure that all software, firmware, and devices are up-to-date.
  Network Monitoring: Continuous monitoring of traffic to detect unusual activities.
  Backup and Recovery Plan: Regularly backup critical data and have a disaster recovery strategy.
Best Practices for Network Security
09